## Slide 1: Content of Lesson 2
Unit 1: Introduction
Unit 2: Individual spatial properties of features
Unit 3: Spatial pattern and neighborhood of features
Unit 4: Weighted spatial pattern and neighborhood
Unit 5: Regionalization
Unit 6: Transformation of spatial features

## Slide 2: Unit 4: Weighted spatial pattern and neighborhood
A: Introduction
B: Weighted spatial pattern and neighborhood
  for point features
  for linear features
  for areal features

## Slide 3
Introduction
1

## Slide 4: Weighted spatial pattern and neighborhood
Our everyday experience suggests that spatial pattern and neighborhood are influenced by thematic properties of features
It is then necessary to combine their geometrical properties with their thematic properties
  This combination is obtained by weighting their geometry as well as the spatial relationships between features
It is therefore necessary to choose a spatial model that integrates the two spatial and thematic dimensions:
  Isotropic weighted space: a space with heterogeneous properties, weighted distance

## Slide 5: Model of space: Isotropic weighted space
Properties within the space are heterogeneous, they influence properties of arrangement and neighborhood:
  spatial and thematic properties should be considered simultaneously
The description of features pattern and neighborhood combines geometric and thematic properties by weighting:
  weighted central tendancy and dispersion
  weighted proximity: weighted distance
Space is modelised as weighted, expressing heterogeneous properties in space
Properties are considered as isotropic:
  they are constant with respect to direction
x
y
z

## Slide 6: Weighting of geometric properties
Neighborhood relationships are describes by indices that combine geometric and thematic properties using weighting
Thematic properties assigned to space locations or features may express:
  the weight of features, expressing their importance, their influence or their attractiviness. Such properties allow the definition of a field of influence for each feature (area of largest weighted proximity)
  the friction of locations in space, expressing the difficulty of access, of movement or the proximity to features (weighted distance)

## Slide 7: Weighting: Weight of features
It is a modification of the metrics:
  wi = weight of feature i
This weighting allows to define a potential field of influence for each of the features:
  space is divided into areas of largest weighted proximity
Geometrical properties are weighted by the relative importance of features
heavy weight
moderate weight
low weight

## Slide 8: Weighting: Proximity to features
It is a modification of the metrics:
  i = 1 / weight of feature i
  so: dpi = di * i
This coefficient of friction allows to define:
  an area of weighted distance to each feature
  the minimum weighted distance from each location in space to features
Further concepts of pathway, barrier (obstacle), force and anisotropy will be considered in Lesson dedicated to accessibility
low friction, high accessibility
moderate friction, moderate accessibility
heavy friction, low accessibility
?
?
Geometrical properties are weighted by the relative friction of accessibility to features

## Slide 9: Description of spatial pattern and neighborhood
Proposed indices of pattern and neighborhood
Indices and statistics of weightedspatial pattern and neighborhood are presented according to the type of spatial features:
  point
  linear
  areal

## Slide 10
2
Weighted spatial pattern and neighborhood of point features

## Slide 11: Point features: Weighted pattern and neighborhood
Different indicators for the spatial distribution and relationships of point features
Spatial distribution description:
  statistical indices of location: central tendency
  statistical indices of dispersion: variability
Neighborhood relationships description:
  weighted distance to features
  areas of largest weighted proximity

## Slide 12: Point features : Example of a distribution
Location and weight of 8 points
Spatial distribution of the 8 points with their respective weight
Point X(m) Y(m) Z(weight)
A 2.0 3.0 4
B 3.0 1.0 1
C 6.0 2.0 1
D 5.0 3.0 4
E 4.0 5.0 1
F 7.0 4.0 1
G 7.0 6.0 1
H 9.0 9.0 4
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Thematic properties of points are heterogeneous. They are considered as relative weights for the computation of spatio-thematic indices
weight = 1
weight = 4
Coordinate X
Coordinate Y

## Slide 13: Point features : Central tendency index
Based on the weighted mean of X and Y coordinates
Mean center MC ( w, w) or ( xw mean, ywmean) :
  it is the weighted center of gravity or the weighted barycenter for the point distribution
wi = thematic value (weight) for point i

## Slide 14: Point features : Weighted mean center
Coordonnée X
Coordonnée Y
Xwmoy
Ywmoy
Weighted mean center
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Yw = 78 / 17 = 4.588
Xw = 91 / 17 = 5.343
Comment:
Compared with the mean center, the weighted mean center is slightly displaced toward H point
Location of the weighted mean center
Location of the mean center

## Slide 15: Point features : Global index of weighted dispersion
Based on the combined dispersion of X and Y coordinates, weighted feature’s properties
Weighted standard distance SDw :
This is a measure of common dispersion in X and Y, with respect to the weighted mean center
wi = thematic value (weight) for point i
Modifier !

## Slide 16: Point features : Weighted standard distance
SDw = 3.723
SDw =  (6.582 + 7.28)
SDw = 3.723
= 6.582
= 7.280
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Computation
Weighted standard distance
Coordinate X
Coordinate Y

## Slide 17: Point features : Weighted neighborhood relationships
The most common neighborhood relationship is the measure of weighted proximity to features
In object mode :
  Areas of largest weighted proximity
    delimited by weighted equidistance line segments between points
    they are polygones
In image mode :
  The weighted distance to the nearest point region
  Regions of largest weighted proximity

## Slide 18: Point objects : Areas of largest proximity
The geometrical proximity to the 8 point features is weighted by their relative influence
Any location within each area is closer to its center than to any other
These areas of largest weighted proximity are called weighted Thiessen ’s or Voronoï ’s polygons
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
The geometrical proximity is weighted by their relative influence
Properties
Areas of largest weighted proximity
Coordinate X
Coordinate Y

## Slide 19: Point regions : Weighted minimum distance
Weighted distance image from each cell to the nearest point region, the weighted minimum distance
The graphical representation suggests limits of areas of largest weighted proximity
Image values express the proximity (weighted distance) to the nearest point region, but without identifying it !
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
A
B
C
D
E
F
G
H
Properties
Weighted minimum distance
Maximum of minimum distances: 1.82
Mean of minimum distances: 0.71
Coordinate X
Coordinate Y

## Slide 20: Point regions : Regions of largest weighted proximity
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
A
B
C
D
E
F
G
H
Image cells are assigned to the point region with the largest weighted proximity
Space is divided into areal regions of largest weighted proximity to their center
Image values identify the point region having the largest weighted proximity. This information adds to the distance value computed above
Properties
Regions of largest weighted proximity
Coordinate X
Coordinate Y
Attribution to the closest point region

## Slide 21
3
Weighted neighborhood of linear features

## Slide 22: Linear features: Weighted spatial neighborhood
Different indicators for the spatial relationships of linear features
Neighborhood relationships description:
  weighted distance to features
  areas and regions of largest weighted proximity

## Slide 23: Linear features: Example of a distribution
Thematic properties of features (weight)
Spatial distribution of the 8 linear features
1
2
3
4
6
5
7
8
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Weight :
1
1.5
2
n : identifier
Coordinate X
Coordinate Y

## Slide 24: Linear objects: Areas of largest weighted proximity
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
6
5
7
8
The space is divided into areas with the largest weighted proximity to each linear feature
Any location within each area is closer to its linear feature than any other
These areas of largest weighted proximity can be associated to the previously presented Thiessen’s or Voronoï ’s polygons
Properties
Areas of largest proximity
The geometrical proximity is weighted by the relative influence of objects
Coordinate X
Coordinate Y

## Slide 25: Linear regions: Weighted minimum distance
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
6
5
7
8
Weighted distance image from each cell to the nearest linear region, the weighted minimum distance
The graphical representation suggests limits of areas of largest weighted proximity
Image values express the proximity (weighted distance) to the nearest linear region, but without identifying it !
Properties
Weighted minimum distance
Maximum of minimum distances: 3.14
Mean of minimum distances: 0.66
Coordinate X
Coordinate Y

## Slide 26: Linear regions: Regions of largest weighted proximity
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
6
5
7
8
Image cells are assigned to the linear region with the largest weighted proximity
Space is divided into areal regions of largest weighted proximity to their linear feature
Image values identify the linear region having the largest weighted proximity. This information adds to the distance value computed above
Attribution to the closest linear region
Properties
Regions of largest weighted proximity
Coordinate X
Coordinate Y

## Slide 27
4
Weighted spatial neighborhood of areal features

## Slide 28: Areal features: Weighted spatial neighborhood
Different indicators for the spatial relationships of areal features
Neighborhood relationships description:
  weighted distance to areal features
  areas and regions of largest weighted proximity

## Slide 29: Areal features: Example of a distribution
Spatial distribution of the 4 areal features with their weight
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
Thematic properties of features (weight)
Weight :
1
1.5
2
n : identifier
Coordinate X
Coordinate Y

## Slide 30: Areal objects: Areas of largest weighted proximity
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
The geometrical proximity to the 4 areal objects is weighted by their relative influence
Any location within each area is closer to its areal feature than to any other
These areas of largest weighted proximity are often called Thiessen’s or Voronoï ’s polygons
Properties
Areas of largest weighted proximity
Areas of largest weighted proximity to the 4 areal features
Coordinate X
Coordinate Y

## Slide 31: Areal regions: Weighted minimum distance
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
Weighted distance image from each cell to the nearest areal region, the weighted minimum distance
The graphical representation suggests limits of areas of largest weighted proximity
Image values express the proximity (weighted distance) to the nearest areal region, but without identifying it !
Properties
Weighted minimum distance
Maximum of minimum distances: 2.92
Mean of minimum distances: 0.61
Coordinate X
Coordinate Y

## Slide 32: Areal regions: Regions of largest weighted proximity
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
Image cells are assigned to the areal region with the largest weighted proximity
Space is divided into areal regions of largest weighted proximity to their areal feature
Image values identify the areal region having the largest weighted proximity. This information adds to the distance value computed above
Attribution to the closest areal region of weighted proximity
Properties
Regions of largest proximity
Coordinate X
Coordinate Y

## Slide 33
End of Unit