## Slide 1: Unit 2: Geometrical properties of individual features
1: Introduction
2: Individual properties (geometry)
3: Spatial pattern (relationships)

## Slide 2
Introduction
1

## Slide 3: Description of spatial properties (1)
Production of indices describing spatial properties
Individual spatial properties:
  Geometry: location, size, shape
Spatial arrangement of features (pattern):
  Spatial relationships: distribution, neighborhood, proximity
Distinction between object mode and image mode:
  object mode: units of observation are features (object)
  image mode : regions are features

## Slide 4: Description of spatial properties (2)
Described spatial features are models of those from the reality
Their geometry is simplified:
  in object mode: through the use of geometrical primitives
  in image mode: through the choice of a resolution
Their attributes corresponds to a global thematic property:
  in object mode: point, linear, areal units
  in image mode: the set of areal units (cells) composing the region

## Slide 5: Description of spatial properties (3)
Descriptors summarize some properties of spatial features
They are indicators (indices):
  expressing some properties, not all
  dependent on the quality of the modeled features
Such indicators should be considered as estimators of properties:
  several indicators can express the same property
  their use and interpretation should be made with sound understanding

## Slide 6
Individual properties of point features
2

## Slide 7: Point features: individual properties
A point feature is modeled as a geometrical point, it has no spatial dimension (0D)
In image mode the point region is also considered as spatially dimensionless, despite the fact it is made of an areal spatial unit (the cell)
Its single individual geometric property is:
  its location

## Slide 8: Point object: Location (position)
Horizontal (X coordinate) and vertical (Y coordinate ) positions in the projected plane, using a defined coordinate system
Example:
  Location of object i: (251.18m, 139.54m)
245 255 265
Coordinate X
147
137
127
Coordinate Y
i
Xi
Yi
Xi = 251.18 Yi = 139.54

## Slide 9: Point region: Location (position)
Horizontal and vertical position :
  located at center of the cell (X,Y coordinates)
  corresponding to the cell position in the grid (column and row)
  grid resolution dependent
Example:
  Location of region i: (251.5m, 139.5m), with a grid resolution of 1m
  or (7,8) in grid coordinates (column, row)
245 255 265
Coordinate X
147
137
127
Coordinate Y
i
Xi
Yi
Xi = 251.5 Yi = 139.5
ou Ci = 7 Ri = 8
20
1
1
20

## Slide 10
3
Individual properties of linear features

## Slide 11: Linear feature: nature and type
A linear feature is modeled as a geometrical broken line or a chain, it has one spatial dimension (1D)
In image mode a linear region is a set of contiguous cells having only one spatial dimension too
A linear feature can be:
  simple: made of a single chain
  complex: made of several chains
A network can be considered either as:
  a single feature (complex linear feature)
  a group of numerous features with connections

## Slide 12: Linear feature: simple and complex
Simple linear object
Object made of a single chain (C1)
Example: a segment
Complex linear object
Object made of several chains (C1, ..., Cn)
Example: a set of segments, a whole network
chain C1
vertex
nod
C1
C2
C3
C4

## Slide 13: Linear feature: individual geometric properties
Only simple linear feature will be discussed here
Set of linear features such as network will be discussed in Lesson « Network description »
Individual geometric properties of a linear feature are:
  its location (position)
  its size (length)
  its shape (sinuosity)
  its orientation (direction)

## Slide 14: Linear object: Location
Generally its location is considered as the horizontal and vertical position into the project plane of its Mean center (MC) or so called Gravity center
Example:
X = 254.4 Y = 134.9
245 255 265
Coordinate X
147
137
127
Coordinate Y
MC
X
Y
(247, 133.5)
(251.5, 136)
(256, 133)
(263, 137)

## Slide 15: Linear object: Size (length)
It is the sum of length of the n segments composing the chain:
  L =  Dsi
  with: Dsi = distance between the two segment i ends (vertices)
Exemple:
245 255 265
Coordinate X
147
137
127
Coordinate Y
L = 5.15+5.41+8.06 = 18.62m
(247, 133.5)
(251.5, 136)
(256, 133)
(263, 137)
s1
s2
s3

## Slide 16: Linear region: Size (length)
It is the sum of length of the n units (cells) composing the region:
This metric uses 2 yardsticks :
  diagonal = 1.41 unit, side = 1 unit
Example:
  Let a grid with 1m resolution:
  L=1.41+1.41+1+1+1+1.41+1.41+1.41+1.41+1.41+1+1.41+1+1.41+1.41
  L = ((10*1.41)+(5*1))*1m = 19.1m
In image mode the estimation of length is systematically exaggerated (see the estimation in object mode: L = 18.62m)
L = ((10*1.41)+(5*1))*1m = 19.1m
245 255 265
Coordinate X
147
137
127
Coordinate Y
20
1
1
20

## Slide 17: Linear object: Shape (sinuosity)
It is the ratio between the chain length L and the distance Ddf between its two ends:
  S = L / Ddf
Interpretation:
  S is a ratio, with S >=1
Example:
245 255 265
Coordinate X
147
137
127
Coordinate Y
L = 5.15+5.41+8.06 = 18.62
Ddf = 16.38
S = 18.62 / 16.38 = 1.14
(247, 133.5)
(251.5, 136)
(256, 133)
(263, 137)
s1
s2
s3
S = 18.62 / 16.38 = 1.14
Ddf

## Slide 18: Linear region: Shape (sinuosity)
It is the ratio between the region length L and the distance Ddf between its 2 ends:
  S = L / Ddf
Interpretation:
  S is a ratio, with S >=1
Example:
L = ((10*1.41)+(5*1))*1m = 19.1m
Ddf = ((4*1.41)+(11*1))*1m = 16.64m
S = 19.1 / 16.64 = 1.15
As these 2 terms L and Ddf use the same metric, the resulting value S is close to the one obtained in object mode (S = 1.14)
S = 19.1 / 16.64 = 1.15
Ddf
245 255 265
Coordinate X
147
137
127
Coordinate Y
20
1
1
20
L

## Slide 19: Linear object: Orientation (direction)
It is the angle of the main direction of the chain with respect to the vertical
  the main direction and the vertical cross at the Mean center (MC)
Example:
  Chain direction:
   = 56°
  It is the same chain as in previous illustration, except its direction is different
 = 56°
245 255 265
Coordinate X
147
137
127
Coordinate Y
MC
X


## Slide 20
4
Individual properties of areal features

## Slide 21: Areal feature: nature and type
An areal object is modeled as a geometrical closen chain (polygon), it has 2 spatial dimensions (2D)
In image mode the areal region is made of a set of contiguous cells having 2 spatial dimensions
An areal feature can be:
  simple: made of a single polygon or region
  complex: made of several polygons (with inner or outer area: island)

## Slide 22: Areal object: simple and complex
Simple areal object
Object made of a single polygon (closed chain)
Convex Concave
Complex areal object
Object made of several polygons (closed chains)
Example: object with inner and outer area (islands)
chain C1
vertex
nod
chain C1
chain C1
chain C2
chain C3

## Slide 23: Areal feature: individual properties
Only simple areal features will be discussed here
Individual geometric properties of an areal feature are:
  its location (position)
  its size (perimeter, area)
  its shape (compactness)

## Slide 24: Objet zonal: Location (position)
Horizontal and vertical position in the projected plane of its Mean center (MC), or so called gravity center
Example:
X = 256 Y = 137.6
MC
X
Y
245 255 265
Coordinate X
147
137
127
Coordinate Y
(252, 143)
(262, 142)
(248, 138)
(255, 132)
(263, 133)

## Slide 25: Areal object: Size (perimeter)
It is the sum of length of the n segments composing the chain:
  L =  Dsi
  with: Dsi = distance between the two segment i ends (vertices)
Example:
L = 6.4+10+9+8.1+9.2 = 42.7m
s1
s2
s3
245 255 265
Coordinate X
147
137
127
Coordinate Y
(252, 143)
(262, 142)
(248, 138)
(255, 132)
(263, 133)
s4
s5

## Slide 26: Areal region: Size (perimeter)
The perimeter can be evaluated with 2 different techniques:
External perimeter of the region (envelop) :
  staircase effect using “Manhattan distance”
  systematic over estimation of the perimeter
Length of the linear region edge (linear perimeter) :
  reduced staircase effect by taking the diagonal distance into account
  under estimation of the perimeter with a too coarse resolution
These two estimation are dependant on the metric used and the grid resolution

## Slide 27: Areal region: Size (perimeter of the envelop)
It is the sum of length of the n cell sides bounding the region:
  This metric distance is often called Manhattan
  yardstick: side = 1 unit
Example:
  Let a grid with 1m resolution (unit):
  L = (50*1)*1m = 50m
In image mode, the use of this metric tends to over estimate the measure of perimeter (see estimation in object mode: L = 42.7m)
L = (50*1)*1m = 50m
245 255 265
Coordinate X
147
137
127
Coordinate Y
20
1
1
20

## Slide 28: Areal region: Size (linear perimeter)
It is the sum of length of the n cells bounding the region :
  This metric uses 2 yardsticks:
  diagonal = 1.41 unit, side = 1 unit
Example:
  Let a grid with 1m resolution (unit):
  L=1.41+1.41+1+1.41+1+1+1+1+1+1+1+1+1+1+1.41+1+1+1+1.41+1+1+1+1+1+1+1+1.41+1+1+1.41+1.41+1.41+1+1.41+1.41
  L = ((11*1.41)+(24*1))*1m = 39.51m
The estimation of perimeter using this technique is close to the one in object mode (L = 42.7m)
L = ((11*1.41)+(24*1))*1m = 39.51m
245 255 265
Coordinate X
147
137
127
Coordinate Y
20
1
1
20

## Slide 29: Areal object: Size (area)
There are several techniques to estimate the area of an object:
For non generalized features (eg. features manually delineated on a map or an image):
  random or regular point sampling technique (Unwin D., 1981, p.126)
  assuming objects are already generalized into polygons, this technique will not be discussed here
For areal objects numerically described with polygons (for a GDB in object mode):
  by breaking up into triangles
  by breaking up into rectangles (computer algorithm)

## Slide 30: Areal object: Size (area) - split into triangles
The area of polygon Ap is the sum of areas of its composing triangles Ati :
  Ap =  Ati
  with: Ati = (B*h) / 2,
  B the basis and h the height
Example:
Ap = 26.82+55.82+36.9 = 119.54m2
245 255 265
Coordinate X
147
137
127
Coordinate Y
T1
T2
T2
Ap = 26.82+55.82+36.9 = 119.54m2

## Slide 31: Areal object: Size (area) - split into rectangles
This technique is adapted for a numerical vector structure (GDB)
Assuming polygon vertices are sequentially described clockwise from a given starting point:
  A = 0.5 *  yi (xi+1 - xi-1)
Example:
A = 0.5 * 239 = 119.5m2
245 255 265
Coordinate X
147
137
127
Coordinate Y
(252, 143)
(262, 142)
(248, 138)
(255, 132)
(263, 133)
A = 0.5 * 239 = 119.5m2
1
2
3
4
5

## Slide 32: Areal region: Size (area)
It is the sum of areas of cells composing the region:
  A = n * Au
  with Au constant for the n units
Example:
  Let a grid with 1m2 resolution (unité):
  A = 110 * 1m2 = 110m2
In image mode, estimation of the the area is close to the one in object mode: (A = 119.5m2)
245 255 265
Coordinate X
147
137
127
Coordinate Y
20
1
1
20
A = 110 * 1m2 = 110m2

## Slide 33: Areal feature: Shape (indices)
The shape of areal features is a very rich concept that is difficult to summarize with a single index
Such indices should allow the comparison between features:
  independant of the description scale and the size of features
  with a reference to a particular shape
This index should be a ratio with at least one reference value

## Slide 34: Areal feature: Shape (compactness indices)
Among the numerous indices proposed in the literature, those describing the compactness of the shape
Counter-example: perimeter / area index (P/A)
  it is simple to produce (based on size indices)
  but its value is dependant on the unit of measurement as well as on the size of features. its use is therefore strongly limited for the comparison of features compactness
A compactness index refers to a geometrically compact shape, such as a circle or sometimes a square

## Slide 35: Basic elements for compactness indices
For the concerned feature:
  A : area of the feature
  L : major axis (distance between the 2 most faraway vertices of the feature)
For the reference feature (circle):
  C : area of smallest circumscribing circle
  RC: radius of smallest circumscribing circle
  I : area of largest inscribed circle
  RI: radius of largest inscribed circle
Example:
  A = 119.5m2 L = D1,4 = 15.8m
  RC= 8m C =  R2 = 201.06m2
  RI= 5.1m I =  R2 = 81.71m2
245 255 265
Coordinate X
147
137
127
Coordinate Y
Rc
Ri
Rc : radius of circumscribing circle C
Ri : radius of inscribed circle I
L : major axis of feature
L

## Slide 36: Areal feature: Compactness indices
Most usual compactness indices are made of:
The ratio between the feature area and the area of its smallest circumscribing circle :
  SA,C = A / C
The ratio between the feature area and the area of a circle having the major axis length L as perimeter :
  SA,L = A /  (0.5 L)2 = 1.27 A / L2
The ratio between the largest inscribed circle area and the area of its smallest circumscribing circle :
  SI,C = I / C

## Slide 37: Areal feature: Compactness indices (continued)
Some other indices derived :
From the ratio between the feature area and the area of its smallest circumscribing circle :
  S’A,C = (A / C) SrA,C = RA / RC, with RA = (A / )
From the ratio between the largest inscribed circle area and the area of its smallest circumscribing circle :
  SrI,C = RI / RC
From the ratio between the minor and the major axis:
  Sl,L = l / L
  with l being the minor axis, perpendicular to the major axis

## Slide 38: Areal feature: Compactness indices (continued)
And some easily computable indices
Some basic elements involved in the computation of compactness are difficult or tedious to produce for irregular features:
  particularly inscribed and circumscribing radius
In numerous GIS software proposed compactness indices are therefore computed as follow:
  SA,Cp = A / Cp , with Cp as the area of a circle having the same perimeter as the feature
  SA,Q = A / Q , with Q as the area of a circumscribing square with a side length equal to L

## Slide 39: Areal feature: Compactness indices - Comparison
Characteristics of the irregular polygon (illustration of the areal object):
A = 119.5, L = 15.8, l = 10.9, P = 42.7, C= 201.06, RC = 8, RI = 5.1

## Slide 40: Areal feature: Compactness indices - Comments
All these indices express the relative compactness of a feature with respect to a compact shape of reference
For all except the last index, the reference is a circular shape :
  the maximum value 1 expresses a maximal compactness
  the lesser the compactness of the polygon, the lower the index value
Each index expresses differently the discrepancy between the feature shape and the reference shape
  It is therefore important to master the meaning of index values

## Slide 41: Areal feature: Compactness indices - References
Suggested references
Baker L., :
Davis P., :
Ebdon D., :
Fitzgerald B., :
Hammond, Mc Cullagh, :
Unwin D., :
Idrisi (Cratio) :
ArcGIS :

## Slide 42
Arrangement spatial des objets ponctuels
5

## Slide 43
Fin de l‘ Unité