## Slide 1: Lesson 2: Discrete spatial variables
Claude Collet
Unit 1: Introduction

## Slide 2: Content of Lesson 2
Unit 1: Introduction
Unit 2: Spatial properties of features
Unit 3: Spatio-attribute properties of features
Unit 4: Regionalisation

## Slide 3: Unit 1: Introduction
1: Definition and example of discrete spatial variables
2: Spatial features
3: Structure of the Lesson
4: Links

## Slide 4
Definition and example of discrete spatial variables (discontinues)
1

## Slide 5: 2 types of spatial distribution of phenomena
During the process of modeling the reality, properties of phenomena are considered as distributed into space in two different manners:
  Continuously: the spatial arrangement of properties produces a continuous surface more or less complex
  Discontinuously or discretely: the spatial arrangement of properties produces spatial features with clearly defined limits (boundaries)

## Slide 6: Example of 2 types of spatial distribution
Continuous distribution
Discontinuous distribution
1: forest
2: culture
3: vineyard
4: swamp
5: lake
6: built up
7: road
8: river
Landcover
Elevation

## Slide 7: The reality is more fuzzy ...
In the real world numerous phenomena lie within these 2 extremes:
  Continuous distribution: one can often observe local discontinuities, such as cliffs in elevation distribution
  Discontinuous or discrete distribution : Limits between features are often fuzzy, such as between forest and grassland, or between waterbody and land

## Slide 8: The reality is more fuzzy ...
Regardless of the nature of a phenomenon, the spatial continuity or discontinuity is decided during the process of modeling the reality :
  The phenomenon of « elevation » can be considered as:
    continuous: spatial properties are then describes as a continuous surface, with a regular mesh of values at an intervall-ratio scale (continuous)
    discontinuous: spatial properties are elevation class values at an ordinal scale (discontinuous), therefore space is organised into regions of same property.

## Slide 9: Continuous or discrete modeling of a phenomenon
Continuous distribution
Elevation (m)
Discontinuous distribution
Classes of elevation

## Slide 10: From the phenomenon to the variable ...
Our objective is to describe and to analyse the spatial distribution of phenomena in the real world
  At information level, properties of a phenomenon are expressed numerically as values of a / several variable(s)
  As properties of variables are located into space, variables are called spatiales variables
  For phenomena with considered discrete spatial distribution, corresponding variables are called discrete spatial variables

## Slide 11: From discrete spatial variable to spatial features
Spatial features can be identified in two different manners:
  Independently from themes (phenomena) to be described: they are a priori features
    Example: Census or administrative units (districts, regions, ...)
  As resulting from the spatial distribution (pattern) of properties for a theme (phenomenon): they are a posteriori features
    Example: Landcover units (areal, linear, point units related with this theme)

## Slide 12: Predefined spatial features (a priori)
Thematicaly independent
The study area is splitted into a fixed number of features, regardless of the considered theme
This division is set as a framework to collect properties for different themes
For each considered theme (phenomenon) global feature properties are collected (regionalisation process)
3 features corresponding to Exemplis counties

## Slide 13: Resulting spatial features (a posteriori)
Thematicaly dependent
The study area is composed with specific number and type of spatial features, related with the considered theme
This division is specific to the considered theme
The production of resulting spatial features assumes the presence of a very dense spatial sample (point or area) in order to construct such spatial features (regionalisation process)
Obviously such division can then be considered as a set of predefined features for the description of other thematic properties

## Slide 14: Examples of predefined features in a study area
10
9
8
7
5
4
2
1
6
3
12
11
10
9
8
7
6
5
4
3
2
1
3) Road segments from a network
2) Landcover features
1) Soil features

## Slide 15
Spatial features (reminder)
2

## Slide 16: Definition of a spatial feature (1)
It is a clearly bounded portion of space
It can express:
  a unit of observation (of measurement)
  a unit of exploitation (resulting from a transformation of units of observation, by agregation ou desagregation)
It can be of 3 types:
  zonal feature
  linear feature
  point feature

## Slide 17: Definition of a spatial feature (2)
1
2
3
4
5
6
7
8
9
10
11
12
Y
X
4
3
2
1
2
1
3
4
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
4
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
4
0
0
0
0
0
0
0
1
1
1
1
1
0
0
4
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
4
0
0
1
1
1
0
0
0
0
0
0
4
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
4
0
0
1
1
1
1
1
1
1
1
1
1
2
2
2
2
2
2
1
1
1
1
1
3
1
1
1
1
1
1
1
1
1
4
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
4
1
1
1
1
1
1
4
1
1
1
1
1
4
1
1
1
1
1
4
1
1
1
1
1
4
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
18
1
1
15
In Object mode
In Image mode
REALITY
Its geometric description is a simplification of its real geometry

## Slide 18: Definition of a spatial feature (3)
In object mode
It is the spatial unit of observation / of measurement
It is geometrically described as:
  a simple or complex polygon, for a zonal feature
  a broken line, for a linear feature
  a point, for a point feature
Its geometry can be describe with a topological or non topological structure
To its geometrical description is associated a data table (containing thematic properties, ...)

## Slide 19: Definition of a spatial feature (4)
In object mode (continued)
The level of details (resolution) of its geometrical description is linked to:
  the description scale of the information source
  the level of generalization defined by the model of reality
  the geometrical complexity of each individual feature
The geometrical resolution is therefore variable and can be adjusted to the complexity of each individual feature

## Slide 20: Definition of a spatial feature (5)
In image mode
It is a set of units of observation / of measurement (the mesh, cell, pixel)
It is defined as a set of contiguous cells sharing the same thematic property (value)
It is called a region (zonal, linear or point)
The thematic property of its components (cells) is stored in the numerical grid:
  it can express either a true thematic property about the feature or its numerical identification (Id)

## Slide 21: Definition of a spatial feature (6)
In image mode (continued)
The level of detail (resolution) of its spatial description is linked to:
  the description scale of the information source (document)
  the level of generalisation decided in the model of reality and applicable to all the layers in the GDB
  the definition of the cell size (unit of observation)
The spatial resolution is therefore fixed for all the units of observation (cells) and the whole set of grids (images) in the GDB

## Slide 22: Example of spatial features in object and image mode
Object mode
Image mode
Linear feature
4
3
2
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
4
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
4
0
0
0
0
0
0
0
1
1
1
1
1
0
0
4
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
4
0
0
1
1
1
0
0
0
0
0
0
4
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
4
0
0
1
1
1
1
1
1
1
1
1
1
2
2
2
2
2
2
1
1
1
1
1
3
1
1
1
1
1
1
1
1
1
4
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
4
1
1
1
1
1
1
4
1
1
1
1
1
4
1
1
1
1
1
4
1
1
1
1
1
4
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
18
1
1
15
Point feature
Areal feature
Linear region
Point region
Areal region

## Slide 23
Structure of the Lesson
3

## Slide 24: Unit 2: Spatial properties of features
Spatial statistics and indices
Individual geometric properties of features:
  point features / regions
  linear features / regions
  areal features / regions
Spatial arrangement (pattern) of a set of features

## Slide 25: Unit 3: Spatio-thematic properties of features
Spatio-thematic statistics and indices
Spatial distribution of spatio-thematic properties:
  point features / regions
  linear features / regions
  areal features / regions
They combine spatial and thematic properties of features

## Slide 26: Diversity of spatial and thematic properties indices

## Slide 27: Unit 4: Regionalisation
Feature properties allocation
From a set of point measurements (sample):
  assigning a representative property to pre-defined features (labelling)
  zoning space into features with homogeneous properties (inference)
For agregated features
For desagregated features

## Slide 28
Allocation
by labelling
What is the thematic property for each feature ?
Zoning
by inference
1
2
3
4
5
6
7
8
10
9
1
3
2
4
5
6
7
9
10
11
14
12
13
15
16
17
8
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
8
13
2
14
5
6

## Slide 29
?
?
?
?
?
10
9
9
12
5
8
6
8
5
Agregation
by grouping
10
11
9
6
7
?
?
?
?
?
?
?
?
?
Desagregation
by inference
What is the thematic property for each feature ?

## Slide 30
Links with - other Lessons - other Modules
4

## Slide 31: Links with other Lessons
Spatial properties: isotropy, anisotropy
  Lesson ?
Spatial dependency: autocorrelation
  Lesson ?
Distance: euclidian (plane), weighted
  Lesson ?

## Slide 32: Links with other Modules
Unit of observation: in object mode, in image mode
  Module B-SM
Sample: sampling process, methods
  Module B-DC
Dimensions: thematic, spatial, temporal
  Module B-SM

## Slide 33
End of Unit 1