## Slide 1: Lesson 2: Discrete spatial variables
Claude Collet
Unit 6: Transformation of spatial features

## Slide 2: Content of Lesson 2
Unit 1: Introduction
Unit 2: Geometrical properties of individual features
Unit 3: Pattern and neighbourhood of spatial features
Unit 4: Weighted spatial pattern and neighbourhood
Unit 5: Regionalization
Unit 6: Transformation of spatial features

## Slide 3: Unit 6: Transformation of spatial features
1: Introduction
2: Aggregation of spatial features
3: Breaking up (disintegration) of spatial features

## Slide 4
Introduction
1

## Slide 5: Transformation of spatial features
It is often necessary to modify original spatial features (objects, cells)
During the constitution of the GDB
  When spatial units of observation do not match the spatial entities defined by the model of reality
During the exploitation of the GDB
  When sets of spatial features are combined or related to each other on the basis of their thematic and spatial properties

## Slide 6: Transformation of spatial features
The reasons for such transformations are related to the mode of description of the reality
In object mode
  The thematic dependency of the spatial feature existence leads to frequent transformations during the exploitation of the GDB
In image mode
  The change in cell resolution during the constitution of the GDB
  The construction of regions from the original units of observation (cells) implies a transformation process

## Slide 7: Transformation of spatial features
The two complementary transformation processes are the “aggregation” and the “breaking up”
Spatial aggregation:
  Spatial features are grouped on the basis of common spatial and/or thematic properties
Spatial breaking up:
  Spatial features are broken apart according to spatial and/or thematic criteria
  From a thematic point of view this action is critical as it implies an inferential process, just like regionalizalisation

## Slide 8: Example of spatial feature transformation processes
What thematic property should be assigned to each derived spatial feature ?
?
?
?
?
?
10
9
9
12
5
8
6
8
5
Aggregation
by generalization
10
11
9
6
7
?
?
?
?
?
?
?
?
?
Breaking up
by
inference
Aggregation process
Breaking up process

## Slide 9
Aggregation: a spatial generalization
2

## Slide 10: Aggregation process
The process of aggregation results in grouping existing spatial features: spatial objects or cells
This process transforms existing spatial features. This rises two major questions:
  Why existing features should be aggregated ?
  What are effects of this aggregation on resulting features ?
    in the spatial dimension
    in the thematic dimension

## Slide 11: Why existing features should be aggregated ?
There are two frequent reasons
To simplify or to generalize units of observation by grouping
  This grouping process can be seen as a spatial scale change (scale reduction)
To simplify or to generalize the diversity of thematic properties
  This grouping process can be seen as a thematic scale change (scale reduction)

## Slide 12: What are effects of aggregation on resulting features ?
Aggregation generates new spatial features. How to derive properties for these resulting features ?
Spatial properties of resulting features can be easily derived
  computation of geometrical, neighbourhood and pattern properties
Thematic properties should express the global behavior of aggregated features
  production of summarizing thematic indices

## Slide 13: Reasons for aggregating features ?
Aggregated features result from:
A grouping based on thematic properties
  aggregation criteria are strictly thematic
A grouping based on spatial properties
  aggregation criteria are strictly spatial
A grouping based on combined thematic and spatial properties
  aggregation criteria are both thematic and spatial

## Slide 14: Thematic criteria of aggregation (1)
Aggregation based on thematic criteria is obtained by grouping properties
The grouping of thematic properties can lead to the aggregation of spatial features sharing the same resulting property
Thematic aggregation can be applied either to spatial objects (object mode) or to cells (image mode)
This aggregation can be restricted by spatial contiguity rule
The effect of this aggregation on spatial entities depends on:
  the extent of the grouping process (diversity reduction)
  the spatial distribution of the resulting properties

## Slide 15: Thematic criteria of aggregation (2)
What thematic properties should assign to resulting features for other measured phenomena ?
When aggregated features are generated, it is then necessary to derive properties for other phenomena from measured properties on original units of observation
Allocation of thematic properties requires the use of operators previously presented in the assignation process:
  central tendency operators: mode, median, mean
  dispersion operators: diversity, inter-quantiles, standard deviation, amplitude, ...

## Slide 16: Thematic criteria of aggregation (3)
What thematic properties to assign to resulting features for other measured phenomena? (cont’d)
However this allocation can involve other specific operators:
  the sum
  operators wheighted by the relative significance of aggregated features:
    wheight of a thematic characteristic (number of inhabitants, …)
    wheight of a spatial characteristic (area, size, …)
    such wheighted operators can be percentage, wheighted mean, …
  In order to define the most appropriated operator to be applied, the nature of the phenomenon (variable) as well as its level of measurement should be considered with great attention

## Slide 17: Thematic criteria of aggregation (4)
Illustration of the aggregation process
1
4
2
3
5
7
8
6
1
2
3
Spatial aggregation
based on a thematic criterion
Thematic allocation
by labeling
Spatial features: Districts
Spatial features: Counties
Allocation method
Sum operator
Weighted operator !
1
2

## Slide 18: Thematic criteria of aggregation (5)
Example of thematic criteria based aggregation
The CORINE Land Cover GDB :
  This European Union database offers 3 different levels of land cover categories:
    level 1 with 5 categories
    level 2 with 15 categories
    level 3 with 44 categories
  The change from level 3 to level 2 or 1 implies a grouping of properties. This leads to the aggregation of original spatial units -contiguous and sharing the same thematic property- into new spatial features.
  For each resulting feature it would then be possible to derive for this land cover theme:
    the central tendency as the modal category
    other indices such as the diversity of original categories

## Slide 19: Thematic criteria of aggregation (6)
Example of thematic criteria based aggregation
Administrative units GDB (Swiss district statistics) :
  Typical national statistics are built at a district level. Such rich databases contain information covering physical social, economical as well as demographical themes.
  Grouping these districts into counties or cantons (states) on the basis their administrative code produces new spatial enties.
  Thematic properties can be derived and assigned to these new features for each original variable in the database:
    the central tendency of aggregated properties using an appropriate statistical operator
    other indicators such as the dispersion index of original properties

## Slide 20: Thematic criteria of aggregation (7)
Practice thematic allocation of aggregated features
Aggregation of “districts” into “counties” :
  Derive thematic properties of aggregated features (counties) for the following variables in the table below
  - Total population: number of inhabitants (Population)
  - % of young resident: <18 year old (% Youths)
  - Major economic sector: 1, 2 or 3 (Economic sector)
  - Landscape quality: 1 to 10 notation (Landscape quality)
  For each variable:
    identify the nature of the phenomenon described by the variable
    define the level of measurement and the measurement unit
    define the aggregation operator to be applied

## Slide 21: Thematic criteria of aggregation (8)
Practice thematic allocation of aggregated features (cont’d)
Original data at “district” level :
Derived data at “county” level :

## Slide 22: Spatial criteria of aggregation (1)
Spatial properties like size, shape or proximity can be used as criteria for aggregating spatial features
The spatial contiguity is one of the most current property used to group features, either alone or combined with other criteria
Scaling change or generalization process make use of spatial criteria
Spatial aggregation can be applied either to spatial objects (object mode) or to cells (image mode)

## Slide 23: Spatial criteria of aggregation (2)
What thematic properties should assign to resulting features for other measured phenomena ?
The process of allocating thematic properties to the aggregated features makes used of the same operators as those presented for thematic based grouping:
  the sum operator
  central tendency operators: mode, median, mean
  dispersion operators: diversity, inter-quantiles, standard deviation, amplitude, ...
  Operators weighted by the relative importance among aggregated features

## Slide 24: Spatial criteria of aggregation (3)
Examples of aggregation process based on spatial criteria
1
2
3
4
6
10
9
8
7
5
A
B
C
D
E
H
G
F
L
K
Q
R
S
P
O
N
M
I
J
19 spatial features
(districts)
Aggregation based on the criteria: - size (>9km2) and - contiguity
produces 10 features
the 4 features (1,6,7,8) in red color were not aggregated
1
2
3
 localisation des 3 services
Aggregation based on the nearest proximity to a service produces 10 features

## Slide 25: Spatial criteria of aggregation (4)
Scale or resolution change by aggregating regular spatial units (cells)
A cell size increase of an image is obtained by an aggregation process
  Cells to be aggregated are contiguous within an aggregation window
The resolution of aggregated cells is a multiple of the original resolution
The allocation of a thematic property to each aggregated cell is obtained by a statistical operator:
  Central tendancy operators: mode, median
  Dispersion operators: diversity, inter-quartile

## Slide 26: Spatial criteria of aggregation (5)
Examples of aggregation process based on spatial criteria :
Scale or resolution change by aggregation for a nominal variable
Cell size
100m
500m
Modal value assigned to resulting cells
Aggregation grid overlayed on original landcover image
Diversity value assigned to resulting cells
1: forest
2: culture
3: vineyard
4: swamp
5: lake
6: built up
7: road
8: river

## Slide 27: Spatial criteria of aggregation (6)
Examples of aggregation process based on spatial criteria :
Scale or resolution change by aggregation for a nominal variable
Cell size
100m
500m
Median value assigned to resulting cells
Aggregation grid overlayed on original 16 elevation classes image
Inter-quartile value assigned to resulting cells

## Slide 28: Spatial and thematic criteria of aggregation (1)
Very often spatial features are grouped based on combined spatial and thematic criteria
The most common spatial criterium is contiguity
  Examples:
  In image mode the “region” is the corresponding concept of “object”. A region is made of a set of contiguous cells sharing the same thematic property (attribute)
  In image mode such concepts as urban district, biotops, watershed or road network assume that their elements share the same thematic property and are spatially contiguous
Other spatial criteria: size, shape, proximity
  Their combination with thematic criteria is often more complex as they can produce different possible aggregation patterns. An optimum should then be considered (see “political redistricting process”)

## Slide 29: Spatial and thematic criteria of aggregation (2)
Example: Production of regions in image mode
Combination of extended contiguity with identical thematic property criteria
Landcover: 150’000 spatial entities
1: forest
2: culture
3: vineyard
4: swamp
5: lake
6: built up
7: road
8: river
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Aggregation into 14 regions

## Slide 30: Spatial and thematic criteria of aggregation (3)
Other examples
Process of political or administrative redistricting
  Examples:
  Existing spatial units should be aggregated into larger features in order to optimize a service, access, ..., or even to guarantee a political majority
Definition of sale territories
  The delineation of sales territories assigned to salesmen is based on thematic criteria such as the density and profiles of potential customers as well as on spatial criteria such as contiguous places and efficient travel path. Such territories can be built based on aggregation of district units for which socio-economical statistics are available.

## Slide 31
Breaking up of spatial features (disintegration)
3

## Slide 32: The process of breaking up
The process of breaking up generates the fragmentation of units of observation: spatial objects or cells
This process transforms existing spatial features. This leads to two types of questions:
  What procedures generate the breaking up of spatial features?
  What are effects of this breaking up on resulting features ?
    about their spatial dimension
    about their thematic dimension

## Slide 33: Reasons for breaking up features
What procedures generate the breaking up of spatial features ?
When two or more sets of spatial features are “overlaid” based on the combination of their thematic or spatial attributes
  This situation is specific to the object mode in which spatial objects are intimately related to themes
When changing to a larger scale (increase resolution)
  This situation mainly occurs in image mode but can be present too in object mode

## Slide 34: Effects of breaking up on spatial information
The breaking up process products new spatial features. How to derive their properties as they were not previously measured ?
Spatial properties of generated features can easily be generated
  Geometrical properties: location, size, shape, ...
  Spatial relationships: pattern, proximity, ...
Thematic properties of new features are more problematic to derive as there is no evidence about their spatial distribution within original units of observation
  An inference process should take place, based on solid assumption about the distribution of the measured property among each “fragment” of the original unit of observation

## Slide 35
End of Unit 6