## Slide 1: Unit 3: Pattern and neighborhood of spatial features
A: Introduction
B: Spatial pattern and neighborhood (relationships)
  for point features
  for linear features
  for areal features

## Slide 2
Introduction
1

## Slide 3: Spatial pattern and neighborhood
Concepts of pattern and neighborhood are complex:
  Only few properties will be considered: central location, dispersion, contiguity, distance, proximity
Different models of space can be related with these concepts:
  Plane isotropic space: homogeneous space, plane distance
  Skew isotropic space: heterogeneous space, weighted distance
  Skew anisotropic space : heterogeneous space with variable properties, weighted directionnal distance
Only the plane isotropic space will be considered in this Unit

## Slide 4: Proximity and distance
Areas of largest proximity
« Field of influence of features »
Minimum distance
« Distance to the closest feature »
Concepts of largest proximity and minimum distance
?
?

## Slide 5: Model of space: Plane isotropic space
Properties within the whole space are either homogeneous or not considered:
  only the spatial dimension is taken into account
Only concepts of plane geometry (euclidian) are used to describe the spatial pattern and neighborhood of features:
  central location, dispersion
  proximity: plane distance (horizontal, euclidian)
Space is modeled as homogeneous and plane, expressing the homogeneity of its properties
In fact properties are ignored:
  the thematic dimension is not considered
x
y

## Slide 6: Description of spatial pattern and neighborhood
Proposed indices of pattern and neighborhood
Indices and statistics of spatial pattern and neighborhood are presented according to the type of spatial features:
  point
  linear
  areal

## Slide 7
Spatial pattern and neighborhood of point features
2

## Slide 8: Point features: Pattern and neighborhood
Different indicators for the spatial distribution and relationships of point features
Spatial distribution description:
  statistical indices of location: central tendency
  statistical indices of dispersion: variability
Spatial pattern description:
  index of spatial pattern
Neighborhood relationships description:
  distance to features, areas of largest proximity

## Slide 9: Point features : Example of a distribution
Location of 8 points
Spatial distribution of 8 points
Coordinate X
Point X (m) Y(m)
A 2.0 3.0
B 3.0 1.0
C 6.0 2.0
D 5.0 3.0
E 4.0 5.0
F 7.0 4.0
G 7.0 6.0
H 9.0 9.0
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Coordinate Y

## Slide 10: Point features : Indices of central tendency
Based on the mean and median of X and Y coordinates
Mean center MC ( , ) or ( xmean, ymean) :
  it is the center of gravity or barycenter of the distribution
Median center Cmed :
  Location of coordinates (Xméd, Yméd)

## Slide 11: Point features : Indices of central tendency
Xmed = 5.5, Ymed = 3.5
Xmed
Ymed
Xmean = 5.375, Ymean = 4.125
Xmean
Ymean
Mean center
Median center
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Coordinate X
Coordinate X
Coordinate Y
Coordinate Y

## Slide 12: Point features : Indices of dispersion
Based on standard deviations and quartiles of X and Y coordinates
Standard deviation of X sx and Y sy :
Interquartile of X xIQ and Y yIQ :
  XIQ = Q3 - Q1 YIQ = Q3 - Q1
  with: Q1 the first quartile and Q3 the third one

## Slide 13: Point features : Indices of dispersion
XIQ = 7 - 3.5 = 3.5
YIQ = 5.5 - 2.5 = 3
sx = 2.326
sy = 2.532
Standard deviation
Interquartiles
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Coordinate X
Coordinate X
Coordinate Y
Coordinate Y

## Slide 14: Point features : Global index of dispersion
Based on the combined dispersion of X and Y coordinates
Standard Distance SD (Bachi distance) :
  It is a measure of the the combined dispersion in X and Y directions, with reference to the mean center
Corriger DS dans équation !

## Slide 15: Point features : Standard distance
SD = 2.37
Computation
Standard distance
SD =  (4.73 + 5.61)
SD = 2.37
= 4.73
= 5.61
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Coordinate X
Coordinate Y

## Slide 16: Point features : Spatial pattern index
Typology of point spatial distributions
clustered
random
systematic
(profiles)
systematic
(contour lines)
systematic
(regular mesh)
Objective: Production of an index expressing these distribution differences
R=0
R=1
R=2.1419

## Slide 17: Point features : Nearest neighbor R index
The nearest neighbor R index compares the observed distribution of points with a theoretically random one.
It is a ratio
R Index :
  Mean distance in the observed distribution:
  Mean distance in the random distribution :
R =
Mean distance between pairs of points sample
Mean distance for a random distribution
di = distance from point i to its nearest neighbor
s : area of the study region
n : number of points
d
dal
=

## Slide 18: Point features : R index - Example
R = 1.212
It is a near random distribution
Computation
Nearest neighbors
dal = 0.5 / ( 8 / (10 * 10) ) = 1.768
d = 17.1422 / 8 = 2.1428
R = 2.1428 / 1.768 = 1.212
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Coordinate X
Coordinate Y

## Slide 19: Point features : Neighborhood relationships
The most common neighborhood relationship is the measure of proximity to features
In object mode :
  Areas of largest proximity
    delimited by equidistance line segments between points (medians)
    they are called Thiessen or Voronoï’s polygons
In image mode :
  The distance to the nearest point region
  Region of largest proximity

## Slide 20: Point objects : Areas of largest proximity
The space is divided into areas delimited by the medians of segments connecting points
Any location within each area is closer to its point center than any other
These areas of largest proximity are called Thiessen or Voronoï ’s polygones
Areas of largest proximity to the 8 points
Properties
Thiessen Polygones
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Coordinate X
Coordinate Y

## Slide 21: Point regions : Minimum distance
Distance image from each cell to the nearest point region, the minimum plane (horizontal, crow fly) distance
The graphical representation suggests limits of areas of largest proximity
Image values express the proximity (distance) to the nearest point region, but without identifying it !
Properties
Minimum plane distance
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Maximum of minimum distances: 6.40
Mean of minimum distances: 1.95
Coordinate X
Coordinate Y

## Slide 22: Point regions : Regions of largest proximity
Image cells are assigned to the point region with the largest proximity
Space is divided into areal regions of largest proximity to their center
Image values identify the point region having the largest proximity. This information adds to the distance value computed above
Properties
Regions of largest proximity
A
B
C
D
E
F
G
H
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Coordinate X
Coordinate Y
Attribution to the closest point region

## Slide 23
3
Spatial pattern and neighborhood of linear features

## Slide 24: Linear features: Pattern and neighborhood
Different indicators for the spatial distribution and relationships of linear features
Spatial pattern description:
  mean size, index of spatial density
Neighborhood relationships description:
  connexity indices of linear features
  distance to features, areas and regions of largest proximity
Connexity indices for linear features organised as a network will be discussed in the Lesson dedicated to accessibility

## Slide 25: Linear features: Example of a distribution
Global description of features
8 linear features (id)
Most are connected and one is isolated :
  1 isolated feature: feature 1
  2 sets of connected features: {2,3,4,5,6}, {7,8}
Each linear feature is simple, made of a single chain with or without vertices (inflexion points)
Spatial distribution of features
1
2
3
4
6
5
7
8
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
n : identifier
Coordinate X
Coordinate Y

## Slide 26: Linear features: Spatial density
Definition
Mean size
  Tm = Lt / n
  with: Lt : total length
  n : number of features
this index expresses the average length of overall features
Density
  D = Lt / A
  with: Lt : total length
  A : area of the region
this index can be used to compare density of several regions
Example
Tm = 27.3 / 8 = 3.413m
D = 27.3 / 100 = 0.273

## Slide 27: Linear features: Connexity index
Definition
C Index of connexity
  C = c / 0.5 n (n-1)
  with: c : number of chains
  n : number of nodes
The denominator expresses the number of 2 by 2 combinations of connections
Comments
Therefore: 0 >= C <= 1
For a planar network with n>3, C could not be equal to 1
Example
In the above example, the set of 8 features contain 11 nodes and 8 chains, C index value is:
C = 8 / 0.5 (11* 10) = 0.15
Comments
The connexity of the whole set is low
Each one of the 3 subsets has a different level of connexity:
  C1 = 1 / 0.5 (2 * 1) = 1
  C 2-6 = 5 / 0.5 (6 * 5) = 0.33
  C 7,8 = 2 / 0.5 (3 * 2) = 0.67
See also Kansky ’s beta and gamma indices

## Slide 28: Linear objects: Areas of largest proximity
The space is divided into areas with the largest proximity to each linear feature
Any location within each area is closer to its linear feature than any other
These areas of largest proximity can be associated to the previously presented Thiessen or Voronoï ’s polygones
Properties
Areas of largest proximity
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
6
5
7
8
Areas of largest proximity to the 8 linear features
Coordinate X
Coordinate Y

## Slide 29: Linear regions: Minimum distance
Distance image from each cell to the nearest linear region, the minimum plane (horizontal, crow fly) distance
The graphical representation suggests limits of areas of largest proximity
Image values express the proximity (distance) to the nearest linear region, but without identifying it !
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
6
5
7
8
Properties
Minimum plane distance
Maximum of minimum distances: 3.61
Mean of minimum distances: 0.95
Coordinate X
Coordinate Y

## Slide 30: Linear regions: Regions of largest proximity
Image cells are assigned to the linear region with the largest proximity
Space is divided into areal regions of largest proximity to their linear feature
Image values identify the linear region having the largest proximity. This information adds to the distance value computed above
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
6
5
7
8
Attribution to the closest linear region
Properties
Regions of largest proximity
Coordinate X
Coordinate Y

## Slide 31
4
Spatial pattern and neighborhood of areal features

## Slide 32: Areal features: Pattern and neighborhood
Different indicators for the spatial distribution and relationships of areal features
Spatial pattern description:
  indices of size, index of spatial density
Neighborhood relationships description:
  areas of largest proximity
  distance to features, regions of largest proximity
Proposed density indices are just a selection of indices used in landscape analysis (see Fragstats)

## Slide 33: Areal features: Example of a distribution
Global description of features
4 areal features (id)
Some are contiguous and some other isolated :
  2 isolated features: 1 and 2
  2 contiguous features: 3 and 4
Each areal feature is simple, made of a single chain (no inner or outer islands)
Spatial distribution of features
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
n : identifier
Coordinate X
Coordinate Y

## Slide 34: Areal features: Pattern indices (1)
Context
Landscape analysis
Concepts attached to Landscape analysis are used in this Unit as follow :
  patch : each of the 4 areal features
  class : the set of the 4 areal features
  landscape : the study area
Example
Geometrical properties
  areal features
  study area
  Perimeter = 4 x 10 = 40m
  Area = 10 x 10 = 100m2
Feature Perimeter Area
1 5.065 1.5
2 10.929 8.25
3 8.349 4.63
4 10.329 7.25
Class 31.512 * 21.63
* The perimeter value takes into account the contiguity of areas 3 and 4

## Slide 35: Areal features: Pattern indices (2)
Definition
Number of areas (NP)
  NP = number of features
Density (PD)
  PD = NP / AR
  with: AR : area of the region
Extensivity (%Land)
  %Land = 100 (AC / AR)
  with: AC : area of the class
Mean size (MPS)
  MPS = AC / NP
Size variability (PSSD)
  PSSD = standard deviation of the area (acreage)
Example
Number of areas (NP)
  NP = 4
Density (PD)
  PD = 4 / 100 = 0.04
Extensivity (%Land)
  %Land = 100(21.63/100) = 21.63%
Mean size (MPS)
  MPS = 21.63 / 4 = 5.41m2
Size variability (PSSD)
  PSSD = 27.12/3 = 3.01
The derived coefficient of variation (PSSD / MPS) allows to compare different pattern distributions

## Slide 36: Areal objects: Areas of largest proximity
The space is divided into areas with the largest proximity to each areal feature
Any location within each area is closer to its areal feature than any other
These areas of largest proximity can be associated to the previously presented Thiessen or Voronoï ’s polygones
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Properties
Areas of largest proximity
Areas of largest proximity to the 4 areal features
Coordinate X
Coordinate Y
1
2
3
4

## Slide 37: Areal regions: Minimum distance
Distance image from each cell to the nearest areal region, the minimum plane (horizontal, crow fly) distance
The graphical representation suggests limits of areas of largest proximity
Image values express the proximity (distance) to the nearest areal region, but without identifying it !
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
1
2
3
4
Properties
Minimum plane distance
Maximum of minimum distances: 2.92
Mean of minimum distances: 0.83
Coordinate X
Coordinate Y

## Slide 38: Linear regions: Regions of largest proximity
Image cells are assigned to the areal region with the largest proximity
Space is divided into areal regions of largest proximity to their areal feature
Image values identify the areal region having the largest proximity. This information adds to the distance value computed above
1
2
3
4
0
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
0
Attribution to the closest areal region
Properties
Regions of largest proximity
Coordinate X
Coordinate Y

## Slide 39
End of Unit